## Slide 1: Computer vision for industrial inspection
NVIDIA DLI

## Slide 2: Workshop Outline
Lab 1 | Automated Optical Inspection and Data Exploration Discuss automatic optical inspection, PCBA process, and current challenges of AOI machines on high false positives Perform EDA on real dataset from GPU production line Scope into short-term DL automation problem
Lab 2 | Model Training with Transfer Learning Apply transfer learning with ResNet-50 architecture Fine-tune the model and set up evaluation metrics Apply augmentation technique to solve heavily imbalanced dataset Examine a confusion matrix and fine-tune results based on domain-expert tunable thresholding
Lab 3 | Model Deployment for Inference Compile trained ResNet-50 model as TensorRT engine Deploy TRT engine to Triton Inference Server Experiment various inference configurations to optimize performance
Assessment | 

## Slide 3: Challenges with AOI
Very High False Positive Rate & Non-Robust/Non-Reliable Detection Require Human Verification
AOI machine employs traditional CV algorithms
False positive rate can be up to 70%
  Reduced throughput
  Requires tedious manual inspection by human operator
  Reliability problems
  Increased cost
Requires frequent and costly manual algorithm tuning
???

## Slide 4: DL-Based Solution Development workflow
Rapid Prototyping for Production
Gather Data
Model Development
Training
Data Curation
Deployment
Monitoring
Model Evaluation
Inference
Data Curation
Experimentation
Validation
Not Satisfied
Data Drift Detected
Re-train
Satisfied
Train Set
Validation Set
Define the Problem
Scoping
Deployment

## Slide 5
Lab 1 - Automatic Optical Inspection and Data Exploration
Lab 2 – Model Training with Transfer Learning Apply augmentation technique to solve heavily imbalanced dataset Apply transfer learning with ResNet-50 Fine-tune the model and set up evaluation metrics Examine a confusion matrix and fine-tune results based on domain-expert tunable thresholding
Lab 3 – Model Deployment for Inference
Assessment
AGENDA

## Slide 6: NVIDIA Train Adapt Optimize (TAO) Toolkit
Simplifies the AI/ML Model Development Workflow
Workflow:
Download pre-trained model
Prepare the data
Efficiently train model
Evaluate model performance
Export model

## Slide 7: Using Transfer Learning
“If I have seen further, it is by standing on the shoulders of giants.”
-Isaac Newton
Transfer Learning abstracts and accelerates deep learning training by allowing developers to fine-tune the pre-trained models (that are domain-specific), instead of going through the time-consuming process of building Deep Neural Networks (DNNs) from scratch

## Slide 8: Stand on top of it and perfect it!

## Slide 9: How a deep neural network sees
Transferring Learned Features from One Model to Another

## Slide 10: Transfer Learning Explained
B Takes Advantage of First Layers Trained in A and Last Layers are Re-Trained for New Task
Start with a pre-trained deep learning model
  Within the neural network are layers that are used to identify outlines, curves, lines, and other identifying features
Delete what’s known as the “loss output” layer, which is the final layer used to make predictions, and replace it with a new loss output layer for custom prediction
  Apply additional training by feeding labeled training data for custom task
  This loss output layer is a fine-tuning node for determining how training penalizes deviations from the labeled data and the predicted output

## Slide 11: Benefits of Transfer Learning
Shorten the lengthy process of training a large model with potentially tens of millions of parameters
Reduce cost of acquiring the amount of data to train a full model as it is often prohibitively expensive in industrial use cases
Reduce the amount of data needed for training under the constraint of not enough data

## Slide 12: NGC – NVIDIA GPU CLOUD
Pre-Trained Models From the NGC Catalog Cover a Wide Set of Use Cases
Image classification supports various backbones such as resnet, vgg, googlenet, mobilenet, squeezenet, darknet, efficientnet, and cspdarknet

## Slide 13: Model evaluation
Accuracy rate provides an overview of how well the model is performing:
  True Positive (TP): model correctly classifies the input as defect
  False Positive (FP): model incorrectly classifies the input as defect
  False Negative (FN): model incorrectly fails to classify the input as defect
  True Negative (TN): model correctly fails to classify the input as defect
We need more insights into accuracy, especially if the dataset is imbalanced, and we need to compromise some aspects of accuracy rate in favor of others
How to Measure Model Accuracy

## Slide 14: Model Evaluation
Precision – the model’s ability to identify the relevant samples only
Recall - the model’s ability to identify all true positive samples of the dataset
F1-Score – harmonic mean of precision and recall
  Is generally considered a better overall measurement than accuracy when an uneven class distribution exists
Precision, Recall, and F1 Score

## Slide 15: ROC Curve
ROC Curve Shows Performance of a Classification Model at All Classification Thresholds
The method was originally developed for operators of military radar receivers during World War II
Created by plotting the true positive rate (TPR) against the false positive rate (FPR) at various thresholds, which depicts relative trade-offs between the two
Provides tools to select possibly optimal model and/or classification threshold

## Slide 16: Fine-Tuning Model
Iteratively Curate Data to Improve Model Performance
Train Model
Error Analysis
Tune Model and Data

## Slide 17: Data Augmentation
Artificially increase sample size by introducing random perturbations like change of color, temperature, flipping, translation, and so on.
In practice they often marginally improve performance
Augmentation can be done online during training or offline
Data Can Be Rare and Expensive to Acquire

## Slide 18: End of lab 2

## Slide 19: Lab 1 Summary
Discuss Automatic Optical Inspection, PCBA process, current challenges of AOI machines on high false positives
Analyze, manipulate, and visualize real dataset from GPU production line
Examine labeling of data obtained from AOI machine and curating dataset further
Scope into short-term DL automation problem

## Slide 20: Lab 2 summary
Apply transfer learning with ResNet-50 to train a custom classification model
Download pre-trained model/architecture from NGC
Apply augmentation technique to solve heavily imbalanced dataset
Fine-tune the model and setup evaluation metrics
Examine a confusion matrix and fine-tune results based on domain-expert tunable thresholding
Iterate “data curation – model training – error analysis” to further improve performance and reduce false positive rate

## Slide 21: What’s Next (Lab 3)
Compile trained ResNet-50 model as TensorRT engine
Deploy TRT engine to Triton Inference Server
Send inference request to server
Compare the performance improvement using various inference configuration